## Slide 1
Embedded Computing Systems
Unit – I-Instruction Set
Text Books:
Wayne Wolf: Computers as Components, Principles of Embedded Computing Systems Design, 2nd Edition, Elsevier, 2008.

## Slide 2
UNIT-I : Instruction Sets, CPUs
Preliminaries
ARM Processor

## Slide 3: PRELIMINARIES
interface
to the
Instruction Sets – These are the programmer’s hardware.
An ARM processor is one of a family of CPUs based on the RISC (reduced instruction set computer) architecture developed by Advanced RISC Machines (ARM). ... ARM processors are extensively used in consumer electronic devices such as smartphones, tablets, multimedia players and other mobile devices, such as wearables.

## Slide 4: Computer Architecture Taxonomy
A block diagram for one type of computer is shown in Figure below.
The computing system consists of a Central Processing Unit (CPU) and
a Memory.
Fig 1. A von Neumann Architecture Computer
Fig 2. A Harvard Architecture

## Slide 5: Computer Architecture Taxonomy cont’d…
The memory holds both DATA and INSTRUCTIONS, and can be read or
written when given an address.
A computer whose memory holds both DATA and INSTRUCTIONS is known as a VON NEUMANN MACHINE.
The CPU has several internal REGISTERS that store values used internally.
One of those registers is the Program Counter (PC), which holds the
address of an instruction in memory.
The CPU fetches the instruction from memory, decodes the instruction, and executes it.
The Program Counter does not directly determine what the machine
does next, but only points to an instruction indirectly in memory.
The action of CPU can be changed by changing only the instructions .
It is this separation of the instruction memory from the CPU distinguishes a stored-program computer from a general finite-state machine.

## Slide 6: Computer Architecture Taxonomy cont’d…
An alternative to the von Neumann style of organizing computers is the Harvard Architecture, which is nearly as old as the von Neumann Architecture.
As shown in Figure below, a Harvard machine has separate memories for data and program.
The Program Counter points to program memory, not data memory.
As a result, it is harder to write self-modifying programs (programs that write data values, then use those values as instructions) on Harvard machines.
Fig 2. A Harvard Architecture

## Slide 7: Computer Architecture Taxonomy cont’d…
Harvard Architectures are widely used, as the separation of program and data memories provides higher performance for Digital Signal Processing.
Processing signals in real-time places great strains on the Data Access System in two ways:
Large amounts of data flow through the CPU; and
that data must be processed at precise intervals, not just when the CPU gets around to it.
Data sets that arrive continuously and periodically are called Streaming Data.
Advantage: Having two memories with separate ports provides higher memory bandwidth; not making data and memory compete for the same port also makes it easier to move the data at the proper times.
DSPs constitute a large fraction of all microprocessors sold today, and most of them are based on Harvard architectures.
e.g.: Most of the telephone calls in the world go through at least two DSPs, one
at each end of the phone call.

## Slide 8: Computer Architecture Taxonomy cont’d…
Also Computer Architectures can be organized based on their INSTRUCTIONS and how they are executed.
Many early computer architectures were what is known today as
Complex Instruction Set Computers (CISC).
These machines provided a variety of instructions that may perform very complex tasks like string searching; having a number of different instruction formats of varying lengths.
One of the advances in the development of high-performance microprocessors was the concept of Reduced Instruction Set Computers (RISC) having fewer and simpler instructions.
The instructions were also chosen so that they could be efficiently executed in Pipelined Processors.
Early RISC designs substantially outperformed CISC designs of the period.

## Slide 9: Computer Architecture Taxonomy cont’d…
Computers can also be classified by several characteristics of their instruction sets.
The instruction set of the computer defines the interface between software modules and the underlying hardware.
Instructions can have a variety of characteristics, including:
Fixed vs. Variable length.
Addressing Modes.
Numbers of Operands.
Types of Operations supported.
The set of registers available for use by programs is called the
Programming Model, also known as the Programmer Model.
Note: The CPU has many other registers that are used for internal operations and are unavailable to programmers.

## Slide 10: Assembly Language
Figure below shows a fragment of ARM assembly code having basic features:
One instruction appears per line.
Labels, which give names to memory locations, start in the first column.
Instructions must start in the second column or after to distinguish them from labels.
Comments run from some designated comment character (; in the case of ARM) to the end of the line.
Assembly language follows this relatively structured form to make it easy for the
assembler to parse the program and to consider most aspects of the program
line by line.
An example of ARM Assembly Language
Column 1 Column 2

## Slide 11: Assembly Language cont’d….
Figure below shows the format of an ARM data processing instruction such as an ADD.
For the instruction ADDGT r0,r3,#5
the cond field would be set according to the GT condition (1100), the opcode field would be set to the binary code for the ADD instruction (0100), the first operand register Rn would be set to 3 to represent r3, the destination register Rd would be set to 0 for r0, and the operand 2 field would be set to the immediate value of 5.
Assemblers must also provide some pseudo-ops to help programmers create complete assembly language programs. An example of a pseudo-op is one that allows data values to be loaded into memory locations. These allow constants e.g. to be set into memory.
r0 = 5
r3
Format of ARM data processing instructions

## Slide 12: Assembly Language cont’d….
An example of a memory allocation pseudo-op for ARM is shown in code  BIGBLOCK% 10
Pseudo-ops for Allocating Memory
The ARM % pseudo-op allocates a block of memory of the size specified by the operand and initializes those locations to zero.

## Slide 13: ARM PROCESSOR
ARM is
actually a
family of RISC architectures
that
have been
developed over many years.
The textual description of instructions, is called an assembly language.
ARM instructions are written one per line, starting after the first column.
Comments begin with a semicolon and continue to the end of the line.
A label, giving name to a memory location, comes at the beginning of the line, starting in the first column.
Here is an example:
LDR r0,[r8] ;a comment label ADD r4,r0,r1

## Slide 14: Processor and Memory Organization
ARM7 is a von Neumann Architecture machine, while ARM9 uses a Harvard Architecture.
The possible performance differences may exist for both the Processors.
The ARM architecture supports two basic types of data:
The standard ARM word is 32 bits long.
The word may be divided into four 8-bit bytes.
An Address refers to a byte, not a word.
Therefore, the word 0 in the ARM address space is at location 0, the
word 1 is at 4, the word 2 is at 8,and so on.

## Slide 15: Processor and Memory Organization cont’d….
The ARM processor can be configured at power-up to address the bytes in a word in either little-endian mode (with the lowest-order byte residing in the low-order bits of the word) or big-endian mode (the lowest-order byte stored in the highest bits of the word), as shown in Figure below:

## Slide 16: Data Operations
Arithmetic and logical operations in C are performed in variables.
Variables are implemented as memory locations.
Therefore, to be able to write instructions to perform C expressions and assignments, both arithmetic and logical instructions must be considered as well as instructions for reading and writing memory.
Figure below shows a sample fragment of C code with data
declarations and several assignment statements.
The variables a, b, c, x, y, and z all become data locations in memory.
A C fragment with Data Operations

## Slide 17: Data Operations cont’d….
In the ARM processor, arithmetic and logical operations cannot be performed directly on memory locations.
ARM is a Load-Store Architecture — the data operands must first be loaded into the CPU and
then stored back to main memory to save the results.
Figure below shows the registers in the basic ARM programming model. ARM has 16 general-purpose registers, r0 through r15.
Except for r15, they are identical; any operation that can be done on one of them can be done on the other one also.
The r15 register has the same capabilities as the other registers, but it is also used as the Program Counter.
The Program Counter (PC) should NOT BE OVERWRITTEN for use in data operations.
However, giving the PC the properties of a
General Purpose Register allows the program
be used as an operand in
counter value to computations, which
can make certain
programming tasks easier.

## Slide 18: Data Operations cont’d….
The other important basic register in the programming model is the
Current Program Status Register (CPSR).
This register is set automatically during every arithmetic, logical, or shifting operation.
The top four bits of the CPSR hold the following useful information about the results of that arithmetic/logical operation:
The negative (N) bit is set when the result is negative in two’s- complement arithmetic.
The zero (Z) bit is set when every bit of the result is zero.
The carry (C) bit is set when there is a carry out of the operation.
The overflow(V) bit is set when an arithmetic operation results in an overflow.

## Slide 19: Example
Status bit computation in the ARM:
An ARM word is 32 bits. In C notation, a hexadecimal number starts with 0x, such as 0xffffffff, which is a two’s-complement representation of -1 in a 32-bit word.
Here are some sample calculations:
- 1 + 1 = 0: Written in 32-bit format, this becomes
0xffffffff + 0x1 = 0x0, giving the CPSR value of NZCV = 1001.
0 – 1 = -1: 0x0 - 0x1 = 0xffffffff, with NZCV = 1000.
231 – 1 + 1 = -231: 0x7fffffff + 0x1 = 0x80000000,
with NZCV = 1001.

## Slide 20
Data Operations cont’d…. | 
The basic form of a data instruction is simple: ADD r0,r1,r2 This instruction sets register r0 to the sum of the values stored in r1 and r2 (i.e. r0 = r1 + r2). In addition to specifying registers as sources for operands, instructions may also provide IMMEDIATE operands, which encode a constant value directly in the instruction. For example, ADD r0,r1,#2 sets r0 to “r1 + 2”. The major data operations are summarized in adjacent Figure. | ARM Data Instructions

## Slide 21: Data Operations cont’d….
RSB performs a subtraction with the order of the two operands reversed, so that
RSB r0, r1,r2 sets r0  r2 - r1.
The bit-wise logical operations perform logical AND, OR, and XOR operations (the exclusive or is called EOR).
The BIC instruction stands for bit clear:
BIC r0, r1, r2 sets r0 to r1 and not r2 (r0  r1).
This instruction uses the second source operand as a mask:
Where a bit in the mask is 1, the corresponding bit in the first
source operand is cleared.

## Slide 22: Data Operations cont’d….
The MUL instruction multiplies two values, but with some restrictions:
No operand may be an IMMEDIATE, and the two source operands must be different registers.
The MLA instruction performs a multiply-accumulate operation, particularly useful in matrix operations and signal processing.
The instruction MLA r0,r1,r2,r3 sets r0  r1 x r2 + r3.

## Slide 23: Data Operations cont’d….
The SHIFT operations can be applied to ARITHMETIC and LOGICAL instructions.
The shift modifier is always applied to the second source operand.
A left shift moves bits up toward the most-significant bits (msb), while a right shift moves bits down to the least-significant(lsb) bit in the word.
The LSL and LSR modifiers perform left and right logical shifts, filling the least-significant bits of the operand with zeroes.
The arithmetic shift left is equivalent to an LSL, but the ASR copies the sign bit—if the sign is 0, a 0 is copied, while if the sign is 1, a 1 is copied.
The rotate modifiers always rotate right, moving the bits that fall off the least-significant bit up to the most-significant bit in the word.
The RRX modifier performs a 33-bit rotate, with the CPSR’s C bit being inserted above the sign bit of the word; this allows the carry bit to be included in the rotation.

## Slide 24: Data Operations cont’d….
The instructions in Figure below are comparison operations; they do not modify general-purpose registers but only set the values of the NZCV bits of the CPSR register.
The compare instruction CMP r0, r1 computes r0 – r1, sets the status bits, and throws away the result of the subtraction.
CMN uses an addition to set the status bits.
TST performs a bit-wise AND on the operands, while TEQ
performs an exclusive-or.
ARM Comparison Instructions

## Slide 25: Data Operations cont’d….
Figure below summarizes the ARM move instructions. The instruction MOV r0, r1
sets the value of r0 to the current value of r1 (i.e. r0r1).
The MVN instruction complements the operand bits (one’s complement) during the move.
ARM MOVE instructions

## Slide 26: Data Operations cont’d….
Values are transferred between registers and memory using the load-store instructions summarized in Figure below.
LDRB and STRB load and store bytes rather than whole words, while LDRH and SDRH operate on half-words and LDRSH extends the sign bit on loading.
An ARM address may be 32 bits long. The ARM load and store
instructions do not directly refer to main memory addresses, since a 32-bit address would not fit into an instruction that included an opcode and operands. Instead, the ARM uses register-indirect addressing.

## Slide 27: Data Operations cont’d….
In register-indirect addressing, the value stored in the register is used as the address to be fetched from memory; the result of that fetch is the desired operand value.
Thus, as illustrated in Figure below, if we set r1 = 0 x 100, the instruction LDR r0,[r1]
sets r0 to the value of memory location 0x100.
Similarly, STR r0,[r1] would store the contents of r0 in the memory location whose address is given in r1.

## Slide 28: Data Operations cont’d….
There are several possible variations:
LDR r0,[r1, – r2] loads r0 from the address given by r1 - r2, while LDR r0,[r1, #4] loads r0 from the address r1 + 4.
how to get an address into a register: to be able to set a register to an arbitrary 32-bit value.
In the ARM, the standard way to set a register to an address is by PERFORMING ARITHMETIC on the PROGRAM
COUNTER, which is stored in r15.
By adding or subtracting to the PC a constant equal to the distance between the current instruction and the desired location, the desired address can be generated without performing a load.

## Slide 29: Data Operations cont’d….
The ARM programming system provides
an ADR
pseudo-operation to simplify this step. Thus, as shown in Figure below, if location 0x100 be given the name FOO, then the pseudo-operation ADR r1,FOO can be used to perform the same function of loading r1 with the address 0x100.

## Slide 30: Data Operations cont’d…. An Example:
C assignments in ARM instructions
x = (a + b) - c;
The semicolon (;) begins a comment after an instruction, which continues to the end of that line.
The statement x = (a + b) - c; can be implemented by using r0 for a, r1 for b, r2 for c, and
r3 for x .
Also registers are needed for indirect addressing.
In this case, the same indirect addressing register, r4 will be reused, for each variable load. The code must load the values of a, b, and c into these registers before performing the arithmetic, and it must store the value of x back to memory when it is done.
This code performs the following necessary steps:
ADR r4,a ; get address for a LDR r0,[r4] ; get value of a
ADR r4,b ; get address for b, reusing r4 LDR r1,[r4] ; load value of b
ADD r3,r0,r1 ; set intermediate result for x to a + b ADR r4,c ; get address for c
LDR r2,[r4] ; get value of c
SUB r3,r3,r2 ; complete computation of x ADR r4,x ; get address for x
STR r3,[r4] ; store x at proper location

## Slide 31: Data Operations cont’d…. An Example:
The operation y a ∗ (b + c); can be coded similarly, but in this case more registers be will reuse by using r0 for both a and b, r1 for c, and r2 for y . Once again, we will use r4 to store addresses for indirect addressing.
The resulting code is
ADR r4,b ; get address for b LDR r0,[r4] ; get value of b ADR r4,c ; get address for c LDR r1,[r4] ; get value of c
ADD r2,r0,r1 ; compute partial result of y
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
MUL r2,r2,r0 ; compute final value of y ADR r4,y ; get address for y
STR r2,[r4] ; store value of y at proper location

## Slide 32: Data Operations cont’d…. An Example:
The C statement z = (a << 2) | (b & 15); can be coded using r0 for a and z, r1 for b, and r4 for addresses as follows:
ADR r4,a ; get address for a LDR r0,[r4] ; get value of a
MOV r0,r0,LSL 2 ; perform shift ADR r4,b ; get address for b LDR r1,[r4] ; get value of b
AND r1,r1,#15 ; perform logical AND ORR r1,r0,r1 ; compute final value of z ADR r4,z ; get address for z
STR r1,[r4] ; store value of z

## Slide 33: Data Operations cont’d….
There are three addressing modes: Register, Immediate, and Indirect.
The ARM also supports several forms of base-plus-offset
addressing, which is related to indirect addressing.
But rather than using a register value directly as an address, the register value is added to another value to form the address.
For instance, LDR r0,[r1,#16] loads r0 with the value stored at location r1 + 16.
Here, r1 is referred to as the Base and the immediate value ’16’ the Offset.
When the offset is an immediate, it may have any value up to 4,096; another register may also be used as the offset.

## Slide 34: Data Operations cont’d….
This addressing mode has two other variations: Auto-indexing and
Post-indexing.
Auto-indexing updates the base register, such that LDR r0,[r1,#16]! first adds 16 to the value of r1, and then uses that new value as the address.
The ! operator causes the Base Register to be Updated with the computed address so that it can be used again later.
Auto-indexing instructions will fetch from the same memory location, but auto-indexing modifies the value of the base register r1.
Post-indexing does not perform the offset calculation until after the fetch has been performed.
Consequently, LDR r0,[r1],#16
will load r0 with the value stored at the memory location whose address is given by r1, and then add 16 to r1 and set r1 to the new value. ( r0  [r1] and then r1  [r1] + 16 ).

## Slide 35: Data Operations cont’d…. Flow of Control
The B (branch) instruction is the basic mechanism in ARM for changing the flow of control.
The address that is the destination of the branch is often called the
branch target.
Branches are PC-relative, the branch specifies the offset from the current PC value to the branch target.
The offset is in words, but because the ARM is byte addressable, the offset is multiplied by four (shifted left two bits, actually) to form a byte address.
Thus, the instruction
B #100
will add 400 to the current PC value (word size 4 x 100).

## Slide 36: Data Operations cont’d…. Flow of Control
The ARM allows any instruction, including branches, to be executed conditionally.
This allows branches to be conditional, as well as data operations.
Figure below summarizes the condition codes.
Condition codes in ARM

## Slide 37
Flow of Control cont’d…. Example | 
Implementing an if statement in ARM The following if statement is used as an example: if (a < b) { x = 5; y = c + d; } else x = c – d; The implementation uses two blocks of code, one for the true case and another for the false case. A branch may either fall through to the true case or branch to the false case: | ; compute and test the condition ADR r4,a ; get address for a LDR r0,[r4] ; get value of a ADR r4,b ; get address for b LDR r1,[r4] ; get value of b CMP r0, r1 ; compare a < b BGE fblock ; if a >= b, take branch ; the true block follows MOV r0,#5 ; generate value for x ADR r4,x ; get address for x STR r0,[r4] ; store value of x ADR r4,c ; get address for c LDR r0,[r4] ; get value of c ADR r4,d ; get address for d LDR r1,[r4] ; get value of d ADD r0,r0,r1 ; compute c + d ADR r4,y ; get address for y STR r0,[r4] ; store value of y B after ; branch around the false block ; the false block follows fblock ADR r4,c ; get address for c LDR r0,[r4] ; get value of c ADR r4,d ; get address for d LDR r1,[r4] ; get value of d SUB r0,r0,r1 ; compute c – d ADR r4,x ; get address for x STR r0,[r4] ; store value of x after ... ; code after the if statement

## Slide 38: Implementing the C switch statement in ARM
The switch statement in C takes the form: switch (test)
{
case 0: ... break;
case 1: ... break;
...
}
The above statement could be coded like an if statement by first testing testA, then testB, and so forth. However, it can be more efficiently implemented by using base-plus-offset addressing and building what is known as a branch table:
ADR r2,test ; get address for test LDR r0,[r2] ; load value for test
ADR r1,switchtab ; load address for switch table
LDR r15,[r1,r0,LSL #2]
switchtab DCD case0
DCD case1
...
case0
case1
... ; code for case 0
...
... ; code for case 1
...

## Slide 39: Implementing the C switch statement in ARM cont’d….
This implementation of switch case uses the value of test as an offset into a table, where the table holds the addresses for the blocks of code that implement the various cases.
The heart of this code is the LDR instruction, which packs a lot of functionality into a single instruction:
It shifts the value of r0 left two bits to turn the offset into a word address.
It uses base-plus-offset addressing to add the left- shifted value of test (held in r0) to the address of the base of the table held in r1.
It sets the PC (r15) to the new address computed by the instruction.
Each case is implemented by a block of code that is located elsewhere in memory.
The branch table begins at the location named switchtab.
The DCD statement is a way of loading a 32-bit address into memory at that point, so the branch table holds the addresses of the starting points of the blocks that correspond to the cases.

## Slide 40: THANK YOU
ECS-VII Sem-CSE-VTU: By Dr. K. Satyanarayan Reddy
40